## Slide 1
Thesis Defense
Tolerating Soft Errors in Ternary Content Addressable Memory
Presented By:
Abdullah-Al-Zobayer (1607008 ) Samrat Alam (1607022 )
Supervised By:
Prof. Dr. Kazi Md. Rokibul Alam
Department of Computer Science and Engineering
Khulna University of Engineering & Technology(KUET)

## Slide 2: Outline
Introduction
Related Works
Objectives
Proposed Methodology
Experimental Analysis
Conclusions

## Slide 3: Introduction
Ternary Content Addressable Memory (TCAM) is a specialized type of high speed memory that searches its entire contents in a single clock cycle.
TCAM is vulnerable to soft errors which corrupts the stored bits in the memory.
When reliability is a matter of concern, the soft errors cause the whole system failure.
That is why for tolerating soft errors, we proposed a method to detect and correct these errors for TCAM.

## Slide 4: Related Works
There are few methods which are proposed to tolerate soft error. Let us discuss some of them.
Reviriego et al. [1] method:
    Merit:
        For small data, it can correct all single bit errors
    Demerit:
        It can not correct multiple bit errors.
        For the large data, it can not correct all single bit errors.

## Slide 5: Related Works
Syafalni et al. [2] method:
    Merit:
        It detects and corrects all single bit errors
    Demerit:
        It is relatively costly for using a Static Random Access Memory (SRAM)
Pontarelli et al. [3] filter-based method:
    Merit:
        It detects and corrects all single bit errors
    Demerit:
        Using bloom filter makes it expensive

## Slide 6: Gap in the Research
There are some gap in the previous research works.
      Correct only single bit errors in TCAM
      Need relatively more bit overhead
      Expensive

## Slide 7: Objectives
To propose an efficient soft error detection and correction method for TCAM.
To minimize information redundancy and other overheads without sacrificing error detection ability.

## Slide 8: Contribution
The major contributions of this research are
To correct 100% errors with relatively low redundant bits.
To detect and correct single bit as well as multiple bit errors.

## Slide 9: Proposed Methodology
This method is divided into two parts.
Generating rules from input data in sender end
Error detection and correction in receiver end
Fig. 1: Example of an (8X6) input message (data words).
In sender part:
Let’s see an example, where
n(data word size) = 6
m(number of data words) = 8
k(number of blocks) = 2
p(number of rules) = 3

## Slide 10: Proposed Methodology : Generating rules
Rules | Bit-1’s position in 2nd block | Bit-1’s position in 1st block | Rules for 2nd block | Rules for 1st block
r1 | 000,001,010,011 | 000,001,010,011, 100,100,110,111 | 0XX | XXX
r2 | 000 | 010,011 | 000 | 01X
r3 | 010,011 | 100,101,110,111 | 01X | 1XX
At first, the input message is divided into two blocks.
Then, the rules are generated.
the rules are r1 = 0XXXXX, r2 = 00001X and r3 = 01X1XX
Block 1
Block 2

## Slide 11: Proposed Methodology : Error injection
Lets consider, the input message from the sender is corrupted by soft errors in the transmission medium.
Block 1
Block 2
Fig. 2: Example of erroneous message.

## Slide 12: Proposed Methodology : Error detection and correction
Columns | Bit-1’s position for 1st block | Detecting erroneous bit positions
1 | 000,001,010,011,100,101, 110,111 | 001
2 | 010,011 | 110
3 | 100,101,110,111 | No error!!!
In the receiver part, the receiver program will detect the errors by generating 1’s position from the rules.
Block 1
Block 2
Here are the erroneous bit positions 001 and 110 in 1st column and 2nd column in 1st block of the message.

## Slide 13: Proposed Methodology : Error Free Message
After the error detection and correction in the receiver end, the correct message from the example is shown below
Fig. 3: Error free correct message.

## Slide 14: Proposed Methodology : Flow diagram
Fig. 5: Flow diagram of generating rules
Fig. 6: Flow diagram of error detection and correction

## Slide 15: Proposed Methodology : Circuit Diagram
Fig. 4: Circuit diagram of the proposed method.

## Slide 16
Experimental Analysis
Experimental Setup:
          Intel(R) Core (TM) i7-7700HQ CPU @ 2.80GHz
          16 GB RAM
          Operating system Windows 10 - 64 bit
          CodeBlocks (IDE 16.03)
          Pspice OrCAD for simulation

## Slide 17
Experimental Analysis
Chart: Data word size
| 8 | 16 | 32 | 64
Reviriego et al. [1] | 75 | 50 | 37.5 | 31.25
Proposed Method | 25 | 25 | 25 | 25
Comparison of bit overhead between Reviriego et al. [1] and the proposed method
Chart: 
| 8 | 16 | 32 | 64
Reviriego et al. [1] | 0.016 | 0.019 | 0.02 | 0.021
Proposed Method | 0.016 | 0.02 | 0.021 | 0.022
Comparison of execution time(sec) between Reviriego et al. [1] and the proposed method
Fig. 7: Comparison of bit overhead
Fig. 8: Comparison of execution time(sec).
17

## Slide 18: Experimental Analysis
 | 2 |  | 3 |  | 4 |  | 5 | 
Weight→ | Reviriego et al. [1] | Proposed Method | Reviriego et al. [1] | Proposed Method | Reviriego et al. [1] | Proposed Method | Reviriego et al. [1] | Proposed Method
0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
1 | 50 | 100 | 62.5 | 100 | 75 | 100 | 84.4 | 100
2 | 50 | 100 | 75 | 100 | 87.5 | 100 | 93.8 | 100
≥4 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
 | 2 |  | 3 |  | 4 |  | 5 | 
Weight→ | Reviriego et al. [1] | Proposed Method | Reviriego et al. [1] | Proposed Method | Reviriego et al. [1] | Proposed Method | Reviriego et al. [1] | Proposed Method
0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
1 | 50 | 100 | 62.5 | 100 | 75 | 100 | 84.4 | 100
2 | 50 | 100 | 75 | 100 | 87.5 | 100 | 93.8 | 100
≥4 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
TABLE I: Percentage of correctable single bit-error patterns for block memories

## Slide 19: Conclusions
The main contribution of this method is to correct a hundred percent of soft errors.
This proposed method requires relatively less redundant bits.
It can detect and correct soft errors in both sequential and random data words in TCAM.

## Slide 20: Future Work
In our future work, We will try
To improve our method which will require less time for execution.
To develop this method from volatile to non-volatile.

## Slide 21: Acknowledgment
We are grateful to Prof. Dr. Muhammad Sheikh Sadi sir for assistance in deciding thesis idea.

## Slide 22: Publication
Our thesis work was published in the 2nd International Conference on Robotics, Electrical and Signal Processing Techniques 2021 (ICREST’21). The source is given below.
S. Alam, A. A. Zobayer and M. S. Sadi, "Towards Tolerating Soft Errors in TCAM," 2021 2nd International Conference on Robotics, Electrical and Signal Processing Techniques (ICREST), 2021, pp. 722-726, doi: 10.1109/ICREST51555.2021.9331148.

## Slide 23: References
[1] P. Reviriego, S. Pontarelli and A. Ullah, "Error Detection and Correction in SRAM Emulated TCAMs," in IEEE Transactions on Very Large Scale Integration (VLSI) Systems, vol. 27, no. 2, pp. 486-490, Feb. 2019.
[2] I. Syafalni, T. Sasao, X. Wen, S. Holst and K. Miyase, "Soft-error tolerant TCAMs for high-reliability packet classifications," 2014 IEEE Asia Pacific Conference on Circuits and Systems (APCCAS), Ishigaki, 2014, pp. 471-474.
[3] S. Pontarelli, M. Ottavi, A. Evans and S. Wen, "Error detection in Ternary CAMs using Bloom Filters," 2013 Design, Automation & Test in Europe Conference & Exhibition (DATE), Grenoble, France, 2013, pp. 1474-1479.

## Slide 24
Thank You